HL-6180DW Professional Mono Laser Printers

Up to 40ppm mono print speed (A4) Automatic 2-sided (duplex) printing with booklet feature Up to 1,200 x 1,200dpi resolution Hi-Speed USB 2.0, Wired (10/100/1000 Base-TX) & wireless network (IEEE 802.11b/g/n) Restrict printing activity to individual or groups of users over a network with the Secure Function Lock 2.0 feature PCL6, BR-Script3 (Postscript®3 Language Emulation), IBM Proprinter XL, Epson FX-850 Windows®, Mac, DOS, Linux compatible 500 sheet lower paper tray & 50 sheet Multi-Purpose (MP) tray: Google Cloud Print6, Brother iPrint&Scan7, Cortado Cloud Services support Supplied with 8,000 page mono toner1 & 30,000 page drum (one page per job) Optional 3,500, 8,000 & 12,000 page mono toners1 1Declared yield value in accordance with ISO/IEC19752. 6Must be web connected 7For Android devices running Android 1.6 or later and Apple devices running iOS 2.0 or later

General

Technology			Electrophotographic Laser Printer

Class 1 Laser Product		IEC 60825-1:2007

Processor			StarSapphire 400MHz

Print Speed – Standard (A4)  	40 pages per minute

Print Speed – Duplex (A4)	18 sides per minute (9 sheets per minute)

Resolution			1200 x 1200 dpi, HQ1200(2400 x 600 dpi), 600 x 600 dpi

Memory			128MB (Expandable up to 384MB, using industry standard 1 x DDR2 16bit 144pin memory module)

Interfaces			Hi-Speed USB 2.0, Wireless Network (IEEE 802.11b/g/n) & Wired Network (Network 10/100/1000Base-TX)

First Print Out Time		Less than 8.5 seconds from ready mode

Warm-up Time		Less than 5 seconds from sleep mode

Print Language		PCL6, BR-Script3 (Postscript®3 Language Emulation), IBM Proprinter XL, Epson FX-850

Embedded Fonts (PCL)		66 scalable fonts, 12 bitmap fonts

Embedded Fonts (PS)		66 scalable fonts

Embedded Barcodes (PCL)	Code39, Interleaved 2 of5, FIM(US-PostNet), Post Net(US-PostNet), EAN-8, EAN-13, UPC-A, UPC-E, Codabar, ISBN(EAN), ISBN(UPC-E), Code128(set A, set B, set C), EAN128(set A, set B, set C)

Control Panel

LCD			1 line, 16 digit back-lit LCD screen

Buttons			Go, Cancel, Secure, OK, Back, +, -

Printer Driver

Windows®	Windows 7® (32 & 64 bit editions), Windows Vista® (32 & 64 bit editions), Windows® XP Professional (32 & 64 bit editions), Windows® XP Home Edition, Windows® Server 2008R2, Windows® Server 2008 (32 & 64 bit editions), Windows® Server 2003 (32 & 64 bit editions)

Macintosh		Mac OS X 10.5.8, 10.6.x, 10.7.x or greater

Linux5		CUPS, LPD/LPRng (x86/x64 environment)

Postscript Universal Printer Driver 	Compatible with any network-connected HL-6100 series connecting to a Windows® PC

PCL Universal Printer Driver	Compatible with any network-connected HL-6100 series connecting to a Windows® PC

Printer Driver Functions

N-up Printing3		Reduce up to 2, 4, 9, 16 or 25 A4 pages into just one A4 page

Poster Printing4		Enlarge 1 A4 page into a poster using 4, 9, 16 or 25 A4 pages

Watermark Printing4		Watermark your documents with predefined text or with your own user-defined messages

Macro Printing4	Create & embed custom templates, for example a company logo, which automatically prints on the top of your printed documents.

ID Printing4			Add identification to your printed documents (date & time, short custom message or PC username)

Automatic Duplex Print		Automatic 2-sided printing

Manual Duplex Print4		Manual 2-sided printing (recommended for media not supported by automatic duplex print)

Booklet Printing4		Print documents in A5 booklet format using automatic or manual duplex print

Quite Mode			Reduces the noise of the machine whilst printing (a small reduction in print speed also occurs)

Skip Blank Page4		Ignores any pages blank pages in your documents.

Reprint4			Print the last document that was sent to the machine

Printer Driver Functions

Secure Function Lock 2.0		Restrict printing activity to individual or groups of users over a network.  Compatible with Active Directory for up to 50 users

Secure Print			Protect print jobs with a 4 digit PIN that has to be entered at the control panel of the printer before the print

Setting Lock			Restrict access to the control panel by securing it with a 4 digit PIN

Mobile / Web Based Printing

iPrint&Scan (Android)		Print JPG & PDF files directly from a smart phone or tablet running the Android Operating System (running Android 1.6 or later)

iPrint&Scan (iPad / iPhone / iPod)		Print JPG & PDF files directly from an iPad / iPhone / iPod (running iOS 2.0 or later)

Google Cloud Print		Print most common file types from any Google Cloud print enabled application

Cortado Cloud Print		Print most common file types from any smart phone, tablet or PC running Cortado applications that support Cortado Cloud Print

Network

Wireless Network		IEEE 802.11b/g/n (Infrastructure Mode / Adhoc Mode)

Wired Network		10/100 Base-TX

Network Protocols		TCP/IP (IPv4 and IPv6)

IPv4	ARP, RARP, BOOTP, DHCP, APIPA(Auto IP), WINS/NetBIOS name resolution, DNS Resolver, mDNS, LLMNR responder, LPR/LPD, Custom Raw Port/Port9100, IPP/IPPS, FTP Server, TELNET Server, HTTP/HTTPS server, TFTP client and server, SMTP Client, SNMPv1/v2c/ v3, ICMP, Web Services (Print), CIFS client, SNTP client

IPv6 (off by default) 	NDP, RA, DNS resolver, mDNS, LLMNR responder, LPR/LPD, Custom Raw Port/Port9100, IPP/IPPS, FTP Server, TELNET Server, HTTP/HTTPS server, TFTP client and server, SMTP Client, SNMPv1/v2c/v3, ICMPv6, Web Services (Print), CIFS Client, SNTP Client

Wireless Setup Support	WiFi Protected Setup (WPS) & AirStation One-Touch Secure System  (AOSS)

Wireless Applications	Intel My WiFi Technology & Vertical Pairing

Wireless Network Security	WEP 64/128 bit, WPA-PSK (TKIP/AES), WPA2-PSK (AES), APOP, POP before SMTP, SMTP-AUTH, SSL/TLS (IPPS, HTTPS, SMTP, POP)

Enterprise Wireless Network Security EAP-MD5, EAP-FAST, PEAP, EAP-TLS, EAP-TTLS

Wired Network Security	APOP, POP before SMTP, SMTP-AUTH, SSL/TLS (IPPS, HTTPS, SMTP, POP), SNMP v3, 802.1x (EAP-MD5, EAP-FAST, PEAP, EAP-TLS, EAP-TTLS) & Kerberos

Print Log to Network	Records printing activities from each individual user, including network username, name of document printed and number of pages, to a file on a network.

E-mail Notifications	Automatically have the device send an e-mail to a nominated e-mail address when it requires attention.

IPv4 Restrict	Restrict which network users either can or cannot access the device over the network.

Network Management Utilities

Embedded Web Server		Web based print management software embedded onto the device

BRAdmin Light3 		Setup and LAN management software

Driver Deployment Wizard4	Easily create print drivers for hassle free deployment over your network

BRAdmin Professional 34&5	LAN/WAN management software

Web BRAdmin4&5		Web Based LAN/WAN management software (when installed to Windows, it can be viewed by any OS through a web browser)

Paper Handling2

Standard Tray: 		500 sheets

Multi-Purpose (MP) Tray: 	50 sheets

Optional Lower Tray:		1 x 500 sheets (LT-5400)

Paper Output2

Face Down: 			150 sheets

Face Up (Straight Paper Path): 	1 sheet

Media Specifications

Media Types & Weights

Standard / Optional Trays: 	Plain & recycled paper (between 60 - 105 g/m2 (16 - 28 lb))

Multi-Purpose Tray:		Plain, recycled & bond paper (between 60 - 163g/m2 (16 to 43lb))

Envelope Printing		Yes, from Multi-Purpose (MP) Tray (up to 3 at one time)

Label Printing		Yes, from Multi-Purpose (MP) Tray (accuracy & reliability will depend on the quality & type of labels used)

Media Sizes

Standard / Optional Trays:	A4, Letter, B5(ISO/JIS), A5, A5(Long Edge), B6(ISO), A6, Executive, Legal, Folio (A4 only supported in automatic duplex print mode)

Multi-Purpose Tray:		Width: 76.2mm to 215.9mm (3" to 8.5") x Length: 127mm to 355.6mm (5" to 14")

Supplies

Inbox Toner			Approx. 8,000 pages1

Standard Yield Toner (TN-3330) 	Approx. 3,000 pages1

High Yield Toner (TN-3380) 	Approx. 8,000 pages1

High Yield Toner (TN-3390) 	Approx. 12,000 pages1

Drum (DR-3300)		Approx. 30,000 pages (one page per job)

The frequency of replacement of consumables will vary depending on the complexity of the prints, the percentage of coverage, paper size, page per job, and the type of media.  For example glossy coated paper will result in a shortened life of such supplies.

Accessories

Optional Lower Tray (LT-5400)	500 sheet paper tray (maximum of 1) this is for the HL-6180DW only

Additional Memory		Expandable up to 384MB, using industry standard 1 x DDR2 16bit 144pin memory module (Not available from Brother)

Dimensions & Weights

|  | With Carton | Without Carton (with consumables) |
| --- | --- | --- |
| Dimensions (WxDxH) | 499 x 478 x 411 mm | 371 x 384 x 288 mm |
| Weight | 13.6 kg | 11.5 kg |

Energy Consumption / Sound Levels

|  | Power Consumption (measured at 25oC) | Sound Pressure Level | Sound Power Level |
| --- | --- | --- | --- |
| Active | Average 701W | Less than 59 dBA | Less than 6.83BA |
| Quiet Mode | Average 340W | Less than 54 dBA | Less than 4.56BA |
| Ready | Average 4.9W | Less than 34 dBA | Less than 6.4BA |
| Deep Sleep | Average 0.8W (2.9W when wireless is active) | Inaudible | Inaudible |
| Auto Power Off (Off Mode) | Average 0.50W | Inaudible | Inaudible |

Environment

TEC Value			2.410 kWh / Week

Power Saving		This enables the printer to consume less energy when not in use

Toner Saving		This reduces the toner usage and helps to reduce the total cost of printer ownership

Energy Star			Yes

Blue Angel			Yes

Nordic Swan			Yes

Duty Cycles

Recommended Monthly		1,000 – 5,000 pages monthly print volume

Maximum Monthly	 	100,000 pages monthly print volume

Contents

Toner Cartridge (Approx. 8,000 pages1)

Drum Unit (Approx. 30,000 pages)

Power Supply Cord

Driver Software for Windows® and Mac

Quick Set-up Guide

PC Interface cable NOT included

1Declared yield value in accordance with ISO/IEC19752

2Calculated with 80g/m² paper

3Windows® & Mac® only

4Windows® only

5Optional free download from the Brother Solutions Centre http://solutions.brother.com

6Must be web connected

7For Android devices running Android 1.6 or later and Apple devices running iOS 2.0 or later

HL-6180DWT Professional Mono Laser Printer

Additional on nthe HL-6180DWT Additional 500 sheet lower paper trays giving a total input capacity of 1,050 sheets

Dimensions & Weights

|  | With Carton | Without Carton (with consumables) |
| --- | --- | --- |
| Dimensions (WxDxH) | 664 x 503 x 702 mm | 371 x 384 x 418 mm |
| Weight | 20.9 kg | 14.6 kg |

Energy Consumption / Sound Levels

|  | Power Consumption (measured at 25oC) | Sound Pressure Level | Sound Power Level |
| --- | --- | --- | --- |
| Active | Average 701W | Less than 59 dBA | Less than 6.80BA |
| Quiet Mode | Average 340W | Less than 54 dBA | Less than 4.50BA |
| Ready | Average 4.9W | Less than 34 dBA | Less than 6.4BA |
| Deep Sleep | Average 0.8W (2.9W when wireless is active) | Inaudible | Inaudible |
| Auto Power Off (Off Mode) | Average 0.50W | Inaudible | Inaudible |